## Slide 1: (Almost) Fence-less Persist Ordering
Sara Mahdizadeh Shahri, Armin Vakil, Aasheesh Kolli
MICRO 2020

## Slide 2: Persistent Memories (PM)
Performance
Density
Non-volatility
Byte-addressability

## Slide 3: Failure Atomicity
Updates need to be visible atomically in PM
Alice
Bob
20$
50$
20$
30$
40$
PM

## Slide 4: Failure Atomicity (cont.)
How to guarantee failure atomicity?
Alice
Bob
20$
50$
20$
30$
Failure
PM
Money is lost!

## Slide 5: Failure Atomicity by Undo Logging
How to provide the required ordering primitives more efficiently?
Create and Persist Log
Update Data
Persist Data
Commit
Fence
Fence
Fence
- Undo Logging is a common technique to achieve Failure Atomicity

## Slide 6: Contributions
- x86 memory persistency model
- Inefficient non-temporal temporal ordering
- Enforce unnecessary persist orderings
- Themis
- Provide this order without using fence
- 1.45x speedup over x86 memory persistency model

## Slide 7: Outline
- Background
- x86 Memory Persistency Model
- Themis
- Evaluation

## Slide 8: Memory System Architecture
D$
D$
L2$+LLC
Recovery
Failure
core
core
PM
DRAM

## Slide 9: Memory Persistency Model
Constrains the order of writes to PM
x86 Memory Persistency Model

## Slide 10: x86 Memory Persistency Model
D$
D$
L2$+LLC
Temporal Path
WCB
WCB
Temporal and Non-temporal path are not in sync
Non-temporal Path
PM
core
core
WriteCombining
Buffer
store data clflushopt/clwb
sfence
movnt log
sfence
log
data
DRAM

## Slide 11: Ordering Across Paths
D$
D$
L2$+LLC
WCB
WCB
movnt log
store data
persist data
sfence
How costly is this ordering primitive?
core
core
PM
DRAM
log
data

## Slide 12: Opportunity
Chart: Speedup
| CQ | CTree | Hashmap | LL | PC | RB | Redis | SPS | TATP | TPCC | Vacation | YCSB | Average
x86 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Ideal | 2.2134 | 1.7959 | 2.2915 | 2.6807 | 2.1818 | 2.0139 | 1.2058 | 2.0717 | 1.0869 | 1.1752 | 1.2027 | 1.1757 | 1.674
Better
1.67x speedup by removing the sfence instruction
2.68x
1.67x

## Slide 13: Ordering Across Paths (cont.)
D$
D$
L2$+LLC
WCB
WCB
Can we persist log before data without an sfence?
core
core
WriteCombining
Buffer
PM
DRAM
log
data
movnt log
store data
persist data
sfence

## Slide 14: Analogy
Home
Option #1
Alice: I am home
Bob
Total time = Alice’s trip + Bob’s trip
Alice

## Slide 15: Analogy
Alice: I am home
Option #2
Total time = Bob’s trip
Home
Bob
Alice

## Slide 16: Analogy
Alice: Flat tire! Wait up!
Option #2 (cont.)
Home
Alice
Bob

## Slide 17: Analogy Summary
Themis
Option # 1
Option # 2
Order
Speed
Persistency
Model
Serialize
Simultaneous
Fast
Slow
x86

## Slide 18: Ordering Between Paths (Revisit)
D$
D$
L2$+LLC
WCB
WCB
core
core
WriteCombining
Buffer
PM
DRAM
movnt log
store data
persist data
sfence
log
data
Themis guarantees this order is always preserved

## Slide 19: Themis
A light-weight x86 extension to provide efficient ordering semantics
Persistent non-temporal updates reach PM before any subsequent temporal stores without any intervening fence

## Slide 20: Themis Architecture
D$
D$
L2$+LLC
WCB
WCB
WBB
WBB
Themis allows communication between temporal path(WBB) and non-temporal path(WCB)
PM
WriteBack Buffer
WriteCombining
Buffer
core
core
DRAM

## Slide 21: Enforcing order in Themis
>=
D$
WCB
WBB
tail
head
C
+ current WCB’s tail value
(wcb-tail)
Persistent block can be drained to L2 only when all its prior non-temporal requests are persisted
head’
head’
wcb-tail
wcb-tail
0.75KB overhead

## Slide 22: Themis in Action
>=
D$
WCB
WBB
tail=3
head=1
C
1
3
data,3
movnt log
store data
persist data
head=
CLWB
3
3
Data can be evicted from L1 as all its prior non-temporal requests that have been in WCB are persisted
Common Case
3
tail=2
log
A

## Slide 23: Themis in Action
>=
D$
WCB
WBB
tail=3
head=1
C
1
2
data,3
CLWB
2
2
Uncommon Case
3
log
A
head=2
Data eviction is delayed untill all prior non-temporal requests are persisted
movnt log
store data
persist data

## Slide 24: Experimental Setup
Gem5 Full-System - details in paper
Benchmarks
  Simple Data Structures: Concurrent queue, Hashmap, Linked-list, Persistent cache, SPS. Tree-based Data Structures: C-Tree, Red-Black Tree. TATP and TPCC
Configs
  x86 memory persistency model (baseline)
  Themis
  Ideal

## Slide 25: Speedup
Chart: Speedup
| CQ | CTree | Hashmap | LL | PC | RB | SPS | TATP | TPCC | GMean
x86 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Themis | 1.5708 | 1.3841 | 1.45 | 1.7621 | 1.8701 | 1.2067 | 1.7742 | 1.1282 | 1.19 | 1.4585
Ideal | 1.585 | 1.3927 | 1.45 | 1.7858 | 1.8834 | 1.2131 | 1.7878 | 1.152 | 1.19 | 1.4698
Better
1.87x
1.45x
Ordering is preserved without any significant performance loss

## Slide 26: Sensitivity Analysis: Transaction Size
Chart: Speedup
| CQ | CTree | Hashmap | LL | PC | RB | SPS | GMean
1 | 1.235 | 1.0861 | 1.1682 | 1.2163 | 1.0265 | 1.15 | 1.0582 | 1.1319
16 | 1.4144 | 1.1789 | 1.2877 | 1.536 | 1.7355 | 1.16 | 1.6579 | 1.4087
64 | 1.5708 | 1.3841 | 1.45 | 1.7621 | 1.8701 | 1.2067 | 1.7742 | 1.5576
256 | 1.6929 | 1.5437 | 1.5665 | 1.8731 | 2.0122 | 1.25 | 1.8571 | 1.6673
Themis improvements are higher with larger transactions
Better

## Slide 27: Conclusion
- x86 provides two paths to PM
  - Expensive fence instructions to order across paths
- Themis
  - Implicit ordering guarantees without using an intervening fence instruction
  - 1.45x speedup over x86 memory persistency model

## Slide 28: Thank you!
This presentation and recording belong to the authors. No distribution is allowed without the authors' permission